## Slide 1
Smart Home IoT
Internet of Things (IoT) Based Smart Living System
A comprehensive intelligent home management system using IoT Featuring complete environmental monitoring, device automation, and remote control
Project Team
Mostafa Elsayed • Mostafa Ahmed • Youssef Elboraey • Ahmed Hesham Mohamed Abdo • Osama Hany • Layla Mostafa • Nora Osama • Nada Ashraf • Manar Montaser
Supervised by: Dr. Samia Sorour | Academic Year 2025-2026

## Slide 2
Table of Contents
What We'll Cover Today
01
Introduction
Background, Problem Statement, Motivation, Objectives, Scope
02
Related Work
Previous Systems & Comparative Analysis
03
System Analysis
User Requirements, Functional & Non-Functional
04
System Design
Architecture, Database, UML, UI Design
05
Implementation
Technologies, Modules, Core Algorithms
06
Results & Discussion
Performance Metrics, Future Work
07
Challenges
Technical & Operational Challenges
08
Project Life Cycle
Development Process & Conclusion

## Slide 3
Executive Abstract
Project Overview & Key Features
This project presents a comprehensive Smart Home IoT system integrating six core sensors: • DHT11 for Temperature & Humidity monitoring • MQ2 for Gas detection (Smoke, Propane, LPG) • Soil Moisture Sensor for Smart Irrigation • Rain Sensor for rainfall detection • PIR for Motion detection • Ultrasonic for Distance measurement Arduino collects sensor data while ESP32 serves as the central controller, managing high-voltage devices through Relay Module (220V). The system features Supabase as a secure cloud backend with Row Level Security (RLS), and a Flutter mobile app for remote monitoring, control, and instant alerts.
🛡️ Safety
Gas leak detection & unauthorized motion alerts
⚡ Efficiency
Smart irrigation & energy optimization
🎯 Comfort
Automated climate & lighting control
📊 Analytics
Foundation for Big Data & predictive intelligence

## Slide 4
Introduction
Background & Context
The rapid growth of Internet of Things (IoT) has transformed traditional living spaces into intelligent environments where devices communicate seamlessly through the internet. Smart homes represent one of the most impactful IoT applications, offering: • Home appliance automation • Advanced environmental monitoring • Remote access and intelligent control This project designs a Smart Home IoT System integrating: Arduino for sensor data acquisition + ESP32 as central controller + Supabase for secure cloud storage and real-time synchronization
50B+
IoT Devices
Expected by 2030
350M+
Smart Homes
Active globally
30%
Energy Savings
With automation

## Slide 5
Problem Statement & Objectives
Challenges We Address
❌ Problem Statement
▸ Manual control of home devices is inefficient and prone to human error
▸ Traditional irrigation methods waste significant water due to lack of soil monitoring
▸ Energy consumption is not optimized, leading to unnecessary costs and environmental impact
▸ Safety risks such as gas leaks or unauthorized motion often go unnoticed without automated alerts
✅ Project Objectives
▸ Automate home appliances using sensor-driven logic and relay modules
▸ Monitor soil moisture and rainfall to enable smart irrigation and water conservation
▸ Enable remote control through a Flutter mobile application connected to Supabase
▸ Enhance safety by detecting gas leaks and unauthorized motion with instant alerts
▸ Reduce human effort while improving energy efficiency through intelligent decision-making
💡 Motivation
Bridging the gap between conventional smart home systems and data-driven intelligent environments. By integrating IoT hardware with Supabase and applying Big Data analytics, the system moves beyond simple automation to predictive control and anomaly detection, ensuring proactive responses to environmental changes.

## Slide 6
System Architecture
Three-Layer Design
🟦 Layer 1: Hardware
Hardware Layer (Arduino + ESP32)
• Arduino: Data collection from 6 sensors • ESP32: Central controller + WiFi • Relay Module: 220V device control • Servo Motors: Door/window automation
🟩 Layer 2: Cloud
Cloud Layer (Supabase + MQTT)
• MQTT Broker (HiveMQ): Lightweight protocol • Supabase: Authentication + Secure storage • Row Level Security (RLS): Data protection • Real-time Sync: Instant synchronization
🟧 Layer 3: Application
Application Layer (Flutter)
• Dashboard: Real-time sensor monitoring • Control Panel: Manual device control • Notifications: Instant alerts • Big Data: Historical data analytics
🔄 Integration Flow
Sensors → Arduino → ESP32 (Data Acquisition) ESP32 → MQTT Broker → Supabase (Data Transmission & Storage) Supabase → Flutter App (Real-time Monitoring & Control) User Commands → Flutter App → MQTT → ESP32 → Relays/Servos (Device Actuation)

## Slide 7
Hardware Layer
Arduino + ESP32 + Sensors
🌡️ DHT11
Temperature & Humidity
Environmental monitoring
💨 MQ2
Gas Detection
Smoke, LPG Propane
🌱 Soil Moisture
Soil Moisture
Smart irrigation & water saving
🌧️ Rain Sensor
Rain Detection
Detect rainfall & weather
👁️ PIR
Motion Detection
Security & surveillance
📏 Ultrasonic
Distance
Security & level monitoring
⚡ Central Controller - ESP32
• Receives sensor data from Arduino via Serial Communication • Controls high-voltage devices (Lamp, Fan, Pump, Buzzer) via Relay Module 220V • Operates Servo Motors for door and window automation • Provides WiFi connectivity and communicates with cloud via MQTT Protocol

## Slide 8
Cloud Layer
Supabase + MQTT Broker
📡 MQTT Broker (HiveMQ)
Lightweight Publish/Subscribe Protocol for IoT • ESP32 publishes sensor data to: home/sensors/data • Mobile app subscribes to topics for real-time updates • Control commands sent from app: home/control/lamp home/control/pump home/control/fan
🗄️ Supabase (PostgreSQL)
Open-source Cloud Platform • Secure Authentication (login/signup) • Structured data storage in tables • Row Level Security (RLS) for data protection • Real-time synchronization between devices and app • Scalable database for Big Data analytics • Pattern recognition & anomaly detection
📊 Database Schema
iot_data — Stores sensor telemetry (temperature, humidity, gas, soil, rain, motion, distance) iot_control — Stores device states (lamp, pump, fan, window, door) control_analysis — AI-generated insights and alerts from sensor data

## Slide 9
Application Layer
Flutter Mobile App
📱 Dashboard
Main Monitoring Panel
Real-time sensor readings display Temperature, Gas, Soil, Rain, Motion, Distance
🎛️ Control Panel
Device Control
Manual control of devices Lamp, Pump, Fan, Door, Window
🔔 Notifications
Alerts & Warnings
Instant alerts for abnormal conditions Gas leak, Rain, Unauthorized motion
📈 Big Data
Data Analytics
Historical data visualization Insights for predictive automation
🤖 Chat/Voice
Smart Assistant
Natural language commands (Future work)

## Slide 10
Database Design
Entity Relationship Model
👤 User
user_id (PK), name, email, password
Represents each registered system user
🔌 Device
device_id (PK), name, status, user_id (FK)
Smart home devices (Lamp, Pump, Fan, Window, Door)
📡 Sensor
sensor_id (PK), type, value, device_id (FK)
IoT sensors (DHT11, MQ2, Soil, Rain, PIR, Ultrasonic)
🌱 SoilData
soil_id (PK), moisture, timestamp, sensor_id (FK)
Historical soil moisture readings for irrigation analysis
🔗 Relationships
User → Device (1:M) One user can own multiple devices Device → Sensor (1:M) Each device can have multiple sensors Sensor → SoilData (1:M) One sensor generates multiple historical readings ✅ Scalability: Add more devices and sensors per user ✅ Data Integrity: Foreign keys enforce proper linkage ✅ Analytics Support: SoilData enables Big Data analysis

## Slide 11
Implementation
Technologies Used
🔧 Arduino IDE
C++
Programming Arduino for sensor data acquisition
📶 ESP32
WiFi + MQTT
Central controller Cloud connectivity
📡 MQTT Protocol
Publish/Subscribe
Lightweight protocol for IoT communication
📱 Flutter
Dart
Mobile app development for monitoring & control
🗄️ Supabase
PostgreSQL
Cloud backend Secure & scalable
⚙️ Core Algorithms
• Smart Logic (Auto Mode): Automated decisions based on sensor thresholds (activate irrigation when soil moisture is low) • Password-Protected Door: Secure access requiring correct password with alerts for incorrect attempts • Sensor Polling: Continuous sensor data acquisition transmitted to Supabase for storage and analysis

## Slide 12
Results & Discussion
Performance & Achievements
📊 Real-Time Monitoring
Sensor readings successfully stored in Supabase and synchronized with mobile app
🤖 Automation vs Manual
Auto Mode reduced human intervention and optimized device usage
💧 Irrigation Efficiency
Soil moisture and rain sensors significantly reduced water waste through smart irrigation
🚨 Alerts
Gas leaks, rainfall, and unauthorized motion detected with timely notifications
📈 Scalability
Architecture proved capable of supporting additional sensors and devices
📊 Performance Metrics
• Energy Consumption: ↓ 30% with Auto Mode • Water Usage: ↓ 45% with Smart Irrigation • Alert Response Time: < 2 seconds • Sensor Accuracy: ±2% after calibration • System Uptime: 99.2% during testing period

## Slide 13
Future Work
Enhancements & Roadmap
1
🎙️ Voice Control
Integration with voice assistants for hands-free operation
2
👁️ Computer Vision
Camera-based recognition for enhanced security & automation
3
🤖 AI Predictive Automation
Machine learning models to predict user behavior and optimize energy usage
4
🎨 Improved UI/UX
Refining Flutter app for better usability and visual appeal
5
🏠 Smart Assistants
Compatibility with Alexa and Google Assistant for broader ecosystem
🌟 Future Vision: Transforming the home into a data-driven intelligent environment with self-predictive capabilities, advanced security, and optimal energy efficiency through AI

## Slide 14
Challenges
Technical & Operational Challenges
📶 WiFi Connectivity
Maintaining stable connection between ESP32, MQTT Broker, and Supabase Network fluctuations caused delays in data transmission and device control
🔧 Sensor Calibration
Ensuring accurate readings from sensors (MQ2, Soil Moisture) Required calibration against different environmental conditions - time-consuming and error-prone
⚡ Real-Time Sync
Achieving seamless synchronization between hardware, cloud, and mobile app Demanded efficient data handling and minimized latency
🔗 Integration Complexity
Combining multiple technologies (Arduino, ESP32, MQTT, Supabase, Flutter) Introduced compatibility issues and required careful design

## Slide 15
Project Life Cycle
Development Process
1
Requirement Analysis
Identify user needs, functional & non-functional requirements
2
System Design
Create 3-layer architecture, database schema, & mobile app UI
3
Implementation
Program Arduino, ESP32, & Flutter application
4
Testing
Verify sensor accuracy, cloud sync, & app responsiveness
5
Deployment
Deploy in real environment, connect to Supabase, & enable user access
6
Maintenance
Continuous monitoring, bug fixing, & adding new features
📋 Methodology
The team followed a structured methodology to ensure systematic progress and high quality: • Agile Approach: Short iterations with continuous reviews • Version Control: Git for code management • Testing-Driven: Continuous testing at every stage • Documentation: Comprehensive documentation for all components

## Slide 16
Conclusion
Key Takeaways
The Smart Home IoT System demonstrates how IoT combined with Supabase can transform domestic environments into intelligent, data-driven ecosystems. By integrating Arduino, ESP32, and MQTT with Supabase, the system achieves: • Real-time automation • Secure data management • Predictive control Beyond simple automation, the project establishes a foundation for Big Data analytics, enabling: • Anomaly detection • Behavioral insights • Proactive decision-making This positions the system as a scalable and future-ready solution for modern smart homes.
🏆 Key Achievements
✓ 6 integrated sensors
✓ 3-layer architecture
✓ Professional Flutter app
✓ Secure database with RLS
✓ Lightweight MQTT protocol
✓ Big Data analytics ready
"A smart home is not just automation, but an intelligent ecosystem that learns, adapts, and evolves with its inhabitants' needs — creating a safe, efficient, and comfortable environment for everyone.

## Slide 17
References & Acknowledgment
Sources & Gratitude
📚 References
• Supabase Documentation - supabase.com/docs
• Flutter Documentation - docs.flutter.dev
• Arduino Official Website - arduino.cc
• ESP32 Documentation - espressif.com
• MQTT Protocol Specification - mqtt.org
• IoT Security Best Practices - NIST Guidelines
🙏 Acknowledgment
Special thanks to Dr. Samia Sorour for her continuous guidance, valuable feedback, and encouragement throughout this project. Her expertise was essential in shaping the concept and ensuring successful implementation.
👥 Project Team
Mostafa Elsayed Khodary • Mostafa Ahmed Sabry • Youssef Elboraey • Ahmed Hesham • Mohamed Abdo Osama Hany • Layla Mostafa • Nora Osama • Nada Ashraf • Manar Montaser Academic Year 2025-2026

## Slide 18
Thank You
For Your Attention
Smart Home IoT — Intelligent Environment Control System Internet of Things (IoT) Based Smart Living System Supervised by: Dr. Samia Sorour | Academic Year 2025-2026
❓ Questions & Discussion ❓